## Slide 1
Model-Based Systems Analysis & Engineering for the Sustainable Flight National Partnership
Irian Ordaz
NASA Langley Research Center
January 14, 2026
National Aeronautics and Space Administration
www.nasa.gov

## Slide 2: Topics
Overview
Digital integration
Demonstrations
NASA Research Announcement (NRA)

## Slide 3: Sustainable Flight National Partnership
Next-Generation Capability on the Path to Net-Zero Greenhouse Gas Emissions by 2050
Advance engine efficiency and emission reduction
Enable integrated trajectory optimization
Advance airframe efficiency and manufacturing rate
Enable use of 100% sustainable aviation fuels
Accelerate toward net-zero greenhouse by 2050 through up to 30% energy efficiency improvement
in next-generation transports, 100% sustainable aviation fuel, and optimal trajectories.
Source: AAVP, NASA ARMD
Notes: Source: Jim Heidmann, LaRC Townhall, AAVP, 2/2023

## Slide 4: MBSA&E Vision for the Sustainable Flight National Partnership
A systems-level, digital integration across Sustainable Flight National Partnership (SFNP) projects which will support the assessment, advancement, and adoption of sustainable technologies for 2030s entry into service subsonic transport aircraft concepts
Notes: Objectives:
Develop an open, cross-project, cross-program, external-capable MBSA&E framework building off ARMD investments and capabilities across AAVP/IASP/TACP in support of the SFNP
Conduct coordinated, integrated systems analysis studies in support of SFNP
  Common, open, reference and vision vehicle models
  Technology benefit assessments and sensitivity studies informed by the SFNP demos

## Slide 5: Digital Integration

## Slide 6: Cross-Domain Architecture
Structural decomposition
Requirements verification simulation
System validation
MBSE System Model
UQ Analysis Model
Non-intrusive polynomial chaos expansion
Efficiently estimates uncertainties
Translates MBSA-MBSE parameters
Evaluates mission scenarios and vehicle designs
Executes UQPCE analysis
MBSE Driver
UQ
MBSA&E
MBSE
MBSA Disciplinary Models
MBSA
MagicDraw

## Slide 7: System Modeling Capability in MBSE
MBSE and MBSA coupling enables the integration of research results from all projects to ensure system level aircraft design and mission requirements are satisfied
Developed an MBSE system model of a TTBW aircraft concept and identified data interfaces required to couple MBSE and MBSA/MDAO models into an integrated modeling environment (IME)
Developed an architectural framework using SE principles and MBSE tools to generate a system model, and applied it in an integrated design environment for analysis of a concept aircraft
Approach and Implementation
Used industry and NASA’s SE processes, requirements, standards and best practices to develop the system model, interactions and instantiation in a cross-domain architecture
Architecture, Tools and Methods
Applied models and methods from NASA’s MBSE community of practice, and informed through cross-agency technical interchanges
Knowledge Sharing

## Slide 8: Multi-Fidelity Analysis Capability
Aerodynamics
Propulsion
Mission
Sizing/Structures
Noise
S&C
Geometry
Increasing Complexity/Fidelity
NASTRAN
Cost
&
TACS
SUITCASE
Mphys
TAIL/CS SIZING
STATIC
STABILITY
FLYING QUALITIES
Aviary external subsystem API used to integrate disciplinary components and extend analysis capability for non-conventional concepts for which historical empirical data is not available
Common variable hierarchy and metadata organized using physical decomposition is accessible by all disciplinary components to avoid variable duplication and ensures consistency across disciplines
AIMEE - AIrcraft Modeling and dEscriptive Environment, an abstraction layer that allows automated construction and execution of a framework, provides a common, unified, and descriptive input file, and decouples the problem definition from the architecture/assembly development
Aviary
& ADH
OpenAeroStruct
OpenAeroStruct
NPSS
OpenVSP
Cart3D

## Slide 9: What is Aviary?
Legacy Tool Capabilities
External Tool Integration through API
Open-Source Release
State-of-the-Art Optimization (OpenMDAO)
Aviary is NASA’s next-gen conceptual aircraft design tool
Developed as a partnership between AATT, TTT, and EPFD
“Stars” on Aviary GitHub Repository
Featured article on nasa.gov
Public release of Aviary
Date
GitHub Stars

## Slide 10: AIMEE - AIrcraft Modeling and dEscriptive Environment
A builder and abstraction layer that allows the automated construction and execution of aeronautics framework problems based on Aviary level 2 user interface and external physics-based analysis tools.
          Aviary
Propulsion: Deck, NPSS, PyCycle
Geom: OpenVSP
Cost:
PTIRS
S&C: Statics, CS Sizing, HQ
CG & Inertia
Aero: OAS, VSPAero
Structures: Suitcase, OAS, TACS
Noise: ANOPP
Concepts Library
Repository for aircraft-specific input files
AIMEE
External Subsystems
Unified Input File
Notes: Simplify the construction and execution of Aviary problems
Decouple the problem definition from the architecture/assembly development
Reduce the development workload and setup time to allow the user to focus on problem definition
Reduce the maintenance associated with upstream development that impacts framework assembly
Provide a unified input file

## Slide 11: Aircraft Models
2035 Entry-into-Service
N3CC CONCEPT
gFAN+ ENGINE
TTBW “LIKE” CONCEPT
gFAN+ / N+3 ENGINE
Present Day Technology
BOEING 777-200ER “LIKE”
GE90 ENGINE
BOEING 737 MAX 8 “LIKE”
LEAP 1B ENGINE
BOEING 787-10 “LIKE”
GenX/RR Trent 100 ENGINE
AIRBUS A320 Neo “LIKE”
PW1100 GTF / LEAP-1A ENGINE
MD 90-30 “LIKE”
IAE V2500 ENGINE
Future Technology
ADVANCED CONCEPTS

## Slide 12: Demonstrations
System Level Optimization of Hybrid Electric Aircraft Concept
Minimize fuel burn
Design variables include gross mass, engine mass flow, battery current and capacity, electrical motor max power, and trajectory
Constraints placed on mass residual, state of charge, and trajectory
Aerostructural Optimization (AIAA Aviation 2025)
Minimize fuel burn
Design variables include wing twist, span, gross mass, structural sizing, and trajectory
Constraints placed on mass residual, structural strength, lift, pitching moment trim, and trajectory
Hybrid-Electric Propulsion System Development (AIAA Aviation 2024)
Minimize fuel burn
Design variables include gross mass, trajectory, engine mass flow, max power and current, battery cell discharge rate and total energy capacity
Constraints placed on mass residual, trajectory, throttle, Thevenin voltage, min state of charge, and max power and current
MBSA&E and UQ Integration (AIAA Aviation 2024)
Enables engineers to assess and mitigate uncertainties associated with a system model, design parameters, and constraint inputs, leading to more complete design studies and better-informed decision-making processes
*Simplified MBSA model
Notes: PyCycle, hybridized two-spool turbofan engine by injecting power on the low-pressure shaft by an electric motor/battery system in climb
The motor efficiency is based on a 2D efficiency map using RPM and torque as inputs
  Determines current draw demanded from the battery
  Battery system computes voltage output to motor system which feeds back required current
Battery voltage decreases linearly with state-of-charge (SOC)
  Motor power is integrated over time resulting in total energy used; battery pack is sized to support total energy used with 20% SOC remaining at the end of the mission
Specific battery energy for the baseline is 0.2 kW-hr/kg

## Slide 13: NRA Overview

## Slide 14: NRA Objectives
NRA PoP
Model Based Systems Analysis & Engineering
“Digital Flight Test”
Framework milestone
A key element of the SFNP was the development of an MBSA&E framework to facilitate technology integration and assessment at the system level and enable collaboration through data exchange and model integration between numerous NASA Aeronautics projects and industry partners.
Industry partnership in the development of the MBSA&E framework was needed to:
Develop and incorporate consistent, state-of-the-art methods for systems analysis and systems engineering across all SFNP partners
Establish best practices within the MBSA&E framework for data exchange and model sharing between industry and government
Develop system-level models of SFNP technologies which will be incorporated into the MBSA&E framework for technology evaluation

## Slide 15: NRA Topics
Aircraft Data Hierarchy/Definition
Standard Interface Definition Between Disciplinary Models/Tools
Systems Analysis and Systems Engineering Integration
Comprehensive Model Sharing and Collaboration Approaches
Narrow Model Sharing and Collaboration Approaches
Aircraft and Component/Subsystem Models
Disciplinary Analysis Tool Integration with OpenMDAO
Disciplinary Analysis Tool Development with OpenMDAO
Georgia Tech
Boeing
M4 Engineering
Boeing, Northrop Grumman
Boeing
Boeing
Boeing
Boeing

## Slide 16: Questions?
Publications and Reports