## Slide 1
www.nasa.gov
Distributed Sensing for Advanced Air Mobility in Varying Environments
Approved for Public Release
Session: IS-28, Distributed Data Acquisition and Processing for Advanced Air Mobility I
Chester Dolph (NASA Langley), Dasarath Katragadda (Analytical Mechanics Associates), Bryan Petty (NASA Langley), Corey Ippolito (NASA Ames), George Gorospe (NASA Ames), Thomas Lombaerts (KBR Wyle), Evan Kawamura (NASA Ames), Nelson Brown (NASA Amstrong), Federica Vitiello (University of Naples “Federico II”), Flavia Causa (University of Naples “Federico II”), Roberto Opromolla (University of Naples “Federico II”), Giancarmine Fasano (University of Naples “Federico II”)

## Slide 2: Outline
AAM: Vision and Application
Distributed Sensing
NASA Langley Experiments
NASA Armstrong Experiments
NASA and University of Naples “Federico II” Experiments
Approved for Public Release

## Slide 3
Safe, sustainable, affordable, and accessible aviation for transformational local and intraregional missions
Distribution
Center/Warehouse
Inter-City
eV/STOL
Inter-city
eCTOL
Cargo
Delivery
Air
Ambulance
Cross-metro
Transfer
Airport
Transfer
Cargo
Delivery
Fleet
Operations
Medical
Supply Delivery
Small
Package Delivery
High Density
Corridor
Regional
Network
Rural Operations
Urban Operations
On Demand
Air-Taxi
Advanced Air Mobility (AAM) Mission
Medium Density/Complexity, Collaborative and responsible, automated systems
Low Density/Complexity, Assistive automation
Low Density, Medium Complexity, Comprehensive safety assurance automation
Line Color Legend
Wildfire Fighting
Operations
Courtesy of the NASA AAM Mission Integration Office
Notes: NASA has charted the evolutionary path toward safe flight of unmanned air vehicles in our nation’s airspace, from large UASs in FAA-controlled airspace to NASA’s pioneering development of UTM, the world’s first system of tested technologies for safe, small UAS traffic management.
NASA’s vision is to build on these developments to enable creation of an Advanced Air Mobility system that is safe, economical and environmentally friendly to move people and packages in population centers, forever changing how citizens around the world benefit from aviation.
This new market must be sustainable from the beginning as aviation as a whole continues to improve.
Electric power and propulsion systems will make AAM vehicles quieter, sustainable and more affordable to operate. Technologies for safe operation of AAM systems such as data driven prognostic system wide safety, detect and avoid and vehicle communications are maturing rapidly, getting smaller, more reliable and more capable. Advances in vehicle and operational system autonomy will unlock new uses of these vehicles and improve safety. Advanced airspace management concepts and tools, that expand on the highly successful UTM service based architecture, will enable safe management and integration of all of these users in high traffic areas.
Through our research and the National Campaign demonstrations, the AAM Mission will deliver aircraft, airspace, and infrastructure system and architecture requirements to enable sustainable and scalable medium density advanced air mobility operations.
Includes “rural” and “urban” applications
  Cargo transport, pax-carrying, aerial work, etc.
  eVTOL, sUAS, eCTOL, hybrid-electric, etc.
  Urban Air Mobility (UAM) as a challenging use-case with high benefit
Enabled by electrification and automation
Does not include:
  Supersonic or hypersonic transport
  Existing hub-and-spoke air service with large transport aircraft

## Slide 4: Advanced Air Mobility (AAM): Overview
Urban Air Mobility (UAM)
  “Local” missions up to ~75 miles around metropolitan areas
Low-Altitude Uncrewed Aircraft Systems
  Local missions for aerial work or (small) cargo delivery (e.g., food, small packages)
Regional Air Mobility (RAM)
  “Intraregional” missions up to ~500 miles
AAM is generally enabled by electrification & automation
Many potential uses, including
  Passenger transport
  Cargo/package delivery
  Emergency services/public good (e.g., air ambulance, EMT transport, etc.)
  Aerial work (e.g., infrastructure inspection, photography, tourism, etc.)
Courtesy of the NASA AAM Mission Integration Office Approved for Public Release
Notes: Three primary application categories:
  Urban Air Mobility (UAM)
    “Local” missions up to ~75 miles around metropolitan areas
    Largely novel “vertiport” infrastructure
    Primarily eVTOL aircraft
    1 to ~6 passengers or equivalent cargo
  Low-Altitude Uncrewed Aircraft Systems
    Local missions for aerial work or (small) cargo delivery (e.g., food, small packages)
    Range of required takeoff/landing infrastructure from none to specialized
    Typically VTOL-capable aircraft
  Regional Air Mobility (RAM)
    “Intraregional” missions up to ~500 miles
    Primarily existing (smaller) airports
    Primarily Electric Short Take-Off and Landing (eSTOL) and Conventional Take-Off and Landing (eCTOL) aircraft
    Up to 19 or 30 passengers or equivalent cargo
AAM is generally enabled by electrification & automation
Many potential uses, including
  Passenger transport
  Cargo/package delivery
  Emergency services/public good (e.g., air ambulance, EMT transport, etc.)
  Aerial work (e.g., infrastructure inspection, photography, tourism, etc.)

## Slide 5: Mission Need
Distributed Sensing
Sensors installed on aircraft and infrastructure to detect, track, and classify aerial objects of interest.
Motivation
Enable Onboard Collision Avoidance
Augment Existing Air Traffic Systems
Mitigate Communication Link Dropout
Avoid and Report Non-Cooperative Aircraft
Facilitate Precision Navigation & Landing
Ensure Safe Operations
There is an imminent need to develop distributed sensor-based surveillance methodologies for airspace shared with Small Uncrewed Aircraft Systems (SUAS) and Uncrewed Aircraft Systems (UAS) to enable Advanced Aircraft Mobility and ensure that airspace remains secure.

## Slide 6: Distributed Sensing Overview
C. Ippolito, E. Kawamura, G. Gorospe, W. Holforty, K. Kannan, V. Stepanyan, T. Lombaerts, N. Brown, A. Jaffe and C. Dolph, "A Structurally-Adaptive Framework for Distributed Airborne Sensing over Real-time Collaborative Information Sharing Networks," in AIAA SciTech, Washington DC, 2023.
Approved for Public Release

## Slide 7: Detectors
Morphological Detector
Close Minus Open Filtering
Cross Hair Kernel
Pro: Detects Static Objects well on lower textured backgrounds
Con: Saturates High Texture
Difference Detector
Subtracts Consecutive Frames after correcting for motion of camera
Extract using contour detection
Works from moving SUAS
Con: Detects moving branches
Background Detection
MOG2 background subtraction algorithm
Well established in CV
Con: May not work well on moving camera
U. Seidaliyeva, D. Akhmetov, L. Ilipbayeva and E. T. Matson, Real-Time and Accurate Drone Detection in a Video with a Static Background, vol. 20, Sensors, 2020.
C. Dolph, C. Minwalla, L. Glaab, M. Logan, B. Allen and K. Iftekharuddin, "Detection and Tracking of Aircraft from Small Unmanned Aerial Systems," Journal of Aerospace Information Systems, vol. 18, no. 11, pp. 838-851, 2021.

## Slide 8: Tracking
R. Opromolla and G. Fasano, "Visual-based obstacle detection and tracking, and conflict detection for small UAS sense and avoid," Aerospace Science and Technology, vol. 119, no. 107167, pp. 1-20, 2021.

## Slide 9: NASA Langley Experiments

## Slide 10: Instrumentation
Approved for Public Release

## Slide 11: Operation Control Centers
BVLOS
VLOS

## Slide 12: Instrumentation
Node Description | Camera Model | Camera Resolution (pixels) | Horizontal and vertical Lens FOV (degrees) | Radar model | RADAR FOV (degree)
Building 3 Camera | 123S6C-C | 4096 × 3000 Each camera | 47.3 × 36.1 Each lens | Echoflight | 120 × 80
Ground Tripod | 123S6C-C | 4096 × 3000 | 62.5 × 47.8 | Echoflight | 120 × 50
Rooftop Tripod | 122S6C-C | 4096 × 3000 | 62.5 × 47.8 | Echoflight | 120 × 50
Onboard Payload | 123S6C-C | 4096 × 3000 | 62.5 × 47.8 | Echoflight | 120 × 60
Node | GPS Receiver | Data Logging Computer | Cellular Modem
3 Camera | GPS-RTK-SMA ZED-F9P (Ublox) | 3 Xaviers with Contech Rogue breakout Board | RUTX11
Ground | GPS-RTK-SMA ZED-F9P (Ublox) | Xaviers with Contech Rogue breakout Board | RUTX11
Rooftop | GPS-RTK-SMA ZED-F9P (Ublox) | NUC 11 Performance Mini Desktop Computer, | RUTX11
Onboard Payload | GPS-RTK-SMA ZED-F9P (Ublox) | Xaviers with Contech Rogue breakout Board | RUTX11
Approved for Public Release

## Slide 13: Rooftop Landing

## Slide 14: Armstrong Flight Research Center Experiments

## Slide 15: Armstrong Flight Research Experiments 2025

## Slide 16
Caserta Italy Experiments 2025

## Slide 17: Radar Analysis
Detection Plot
GNSS ground truth Plot
SUAS range computed from by radar and algorithm. Multiple SUAS shown
SUAS range computed via GNSS in sensor coordinate system (ground truth).
Multiple radars placed in proximity

## Slide 18: Conclusion
These experiments help evaluate the generalizability of aircraft detection algorithms against varying targets and backgrounds
  Provide airspace surveillance at vertiports and traffic corridors
  Alternate systems for safety critical AAM flight operations
  Onboard detect and avoid
Future work includes the analysis of these three datasets for developing a generalized airspace surveillance system in support of the AAM mission.

## Slide 19
Questions?
Approved for Public Release