## Slide 1
Advances in Design Capabilities for Planetary Missions from the NASA Entry Modeling and Instrumentation Portfolio Justin Haskins,1 Aaron Brandis,1 Tom West,2 Monica Hughes2
1NASA Ames Research Center
2NASA Langley Research Center 23rd International Planetary Probe Workshop | June 23rd, 2026

## Slide 2: NASA STMD Entry Modeling & Instrumentation Portfolio (EM&I)
Entry System Instrumentation
Entry Systems Modeling
Flight Test and Instrumentation
EM&I is the only NASA portfolio that builds and validates the cross‑cutting flight technologies, models, and tools needed for EDL across missions
Delivers ground‑to‑flight traceability with quantified uncertainty
Reducing mission risk and facilitating faster design iteration
Enabling new entry and descent system architectures
EM&I provides EDL capabilities and expertise resulting from decades of mission-focused development – there is no viable industry counterpart

## Slide 3: Capability Outline by Mission
EM&I modeling impacts on Dragonfly (Titan) will be used to highlight modeling capabilities generally useful for EDL missions:
  Aeroheating of Detailed Geometries
  Capsule Dynamics
  Parachute Dynamics
Capability infusion plans for new and emerging missions will also be discussed:
  DAVINCI (Venus)
  Outer Planets (Uranus and Saturn)

## Slide 4
Highlighting EM&I Capability Infusion for Dragonfly
EM&I partnered with Dragonfly to infuse and demonstrate new capabilities for mission design – mitigation efforts for 5 of 10 major EDL mission risks supported using these developments
Dynamics under Drogue
DrEAM Instrumentation Suite
Dynamic Stability Characterization
Improved Aeroheating Tools

## Slide 5: Aeroheating of Detailed Geometries
‘PICA-tooth’ Shoulder Heating with Coupled Radiation, Flow, and Material Response (Ares Code)
Dragonfly aeroshell has detailed structural features – capabilities for efficient, multiphysics aeroheating analyses reduced design complexity and mitigated aeroheating risks
POC: Olivia Schroeder, Amal Sahai, Joey Schulz, Kyle Thompson, Prakash Shrestha
Design Impact: Coupled flow-material-radiation analyses mitigated need to protect main seal with complex, protective heatshield ‘tooth’
Risk Mitigation: Improved efficiency radiation and CFD algorithms mitigated aeroheating concerns for backshell low-gain antenna (LGA)
LGA Impact on Heating of Full Aeroshell (HyperSolve CFD Solver)
LGA Heating with Coupled Tools (NERO Radiation Code)

## Slide 6: Vehicle Dynamics
Dragonfly poses unique challenges for vehicle dynamics that have not been faced by previous missions – efforts underway to drive down mission risk
Titan atmosphere reaches a higher altitude, is colder, and denser near the surface compared to Mars
Disk-gap-band supersonic drogue parachute 6 minutes after entering the atmosphere at a target Mach number of 1.4 to 1.5
Vehicle will decelerate under drogue for unprecedented > 100 minutes!
Genesis heritage aeroshell (basis for Dragonfly) is known to be dynamically unstable in certain conditions
Genesis Impact and CFD of Dragonfly Capsule

## Slide 7: Vehicle Dynamics - DAWG
POCs: Quincy McKown, Mark Schoenenberger, Ben Libben, Hannah Alpert
The Dynamic Analysis Working Group (DAWG) is working to fuse theoretical, computational, and experimental approaches for dynamics to better predict stability
Current work to fill key missing low-supersonic data – LaRC wind tunnels, SPEED drop tests, Aberdeen testing – to reduce into improved model description near drogue deploy
Longer term aim is to reformulate dynamic stability equations for improved accuracy
Three-pronged DAWG Approach to Stability
SPEED Concept of Operations (Stratospheric Projective Experiment in Entry Dynamics)
Collaborative Dragonfly-NESC-DAWG Aberdeen Ballistic Range Testing

## Slide 8: Parachute Dynamics
Capabilities to simulate coupled drogue deploy and aeroshell dynamics in development
POCs: Francois Cadieux, Michael Barad
Animation showing Mach number on a slice, where the aeroshell and parachute surfaces are shown in gray, and the parachute lines in black.
Simulation of Dragonfly Drogue Deployment (LAVA solver)

## Slide 9: Dragonfly Entry Aerosciences Measurements (DrEAM) Instrumentation Suite
POCs: Helen Hwang & Aaron Brandis
DrEAM Instrumentation Bridges Aeroheating and Dynamics
Notes: Update figure….

## Slide 10
Mission Infusion: DAVINCI (Venus)
Comparison to Flight Data
EM&I will provide entry instrumentation for the DAVINCI capsule through the VISTA project to improve entry modeling in CO2 environments.
Uncoated
Roughness Heating Augmentation
Models for roughness heating are important for Venus entry and largely empirical. EM&I is developing roughness heating augmentation models for both tiled and monolithic TPS.
4000
3000
2000
W/cm2
Venus offers several challenges for EDL, the entry conditions are extreme, leading to the development of new and novel EDL technologies.
Capsule Dynamic Behavior
Free-flight CFD can be used to estimate drag as a function of the trajectory to minimize descent time for Venus descent. (ADEPT shown)
Benchmark Radiative Heating
Radiative heat flux may be dominant for Venus entry. Shock tube data for CO2 atmospheric entry is being generated for model validation.

## Slide 11
Missions to outer planets pose several EDL challenges including the largest heat fluxes of our solar system, multi-destinations within one mission, and new TPS materials.
Mission Infusion: Outer Planets (Saturn, Neptune, Uranus)
Launch to Landing GN&C
Coupled GNC (POST2) and trajectory (MONTE) solver provides insights to multiple mission concepts.
Fracture & Failure of Woven TPS
Developing models for TPS fracture and failure modes to improve reliability prediction and risk reduction for extreme entries.
Advancing Woven TPS Thermal Models
EM&I is developing woven TPS (e.g., HEEET) material models to quantify thermal uncertainties and aid design.
Radiative Heating & Kinetics
Radiative heat flux has large uncertainties for H2/He atmospheres. Shock tube data for H2/He atmospheric entry is being generated for model refinement.
Notes: Tom

## Slide 12: Summary
EM&I seeks to develop new modeling and simulation capabilities for EDL, validated through ground and flight testing
Value of incorporating improved capabilities into missions demonstrated through partnership with Dragonfly
Future activities will be planned as the mission landscape evolves:
  Mars, Outer Planets, Sample Returns, Venus missions

## Slide 13: Summary of Tools
Icarus | Material Response | Limited Distribution
Ares | Multi-physics Coupling | US Distribution
PATO | Material Response | Open Source
PuMA | Micro-Material Response | Open Source
arcjetCV | Arc Jet In Situ Analyses | Open Source
SPARTA | Gas-Surface Interactions | Open Source
NEQAIR | Radiation | NASA Software
NERO | Radiation | To Be Released
HARA | Radiation | NASA Software
MPEC | Quantum Chemistry | NASA Software
LAURA | CFD | NASA Software
HyperSolve | CFD | NASA Software
NASA Software: https://software.nasa.gov/
Contact for More Info: justin.b.haskins@nasa.gov, aaron.m.brandis@nasa.gov
Notes: BEAST… TOMATO… facilities… EAST, ARCTRON,

## Slide 15: Entry, Descent, and Landing (EDL) Challenges
EDL is small portion of mission timeline but among the largest risks
Entry Heating
Aerodynamic Heating
Radiative Heating
Thermal Protection System (TPS) Response
Hypersonic Aero-Maneuvering
Vehicle Dynamics Stability
Guidance, Navigation & Control
Parachute Deployment & Descent
Parachute Stability & Dynamics
Guidance, Navigation & Control
Mars2020 Simplified Entry & Descent
EDL is a multi-stage process unique to mission and destination
Each stage presents challenges – high velocity, large thermal gradients, and complex maneuvers
Test-as-you-fly is usually not feasible – validated models required for ground-to-flight traceability

## Slide 16: Vehicle Dynamics - SPEED
POCs: Ben Libben, Hannah Alpert, Kenny McAfee
The Stratospheric Projectile Experiment of Entry Dynamics (SPEED) is low-cost flight test platform to provide free flight dynamics
SPEED allows testing at Transonic Mach where ground facilities have no mutual overlap – verification of ground tests
First flight test with Dragonfly-like capsules is slated for later this summer - data will be leveraged in DAWG activities to complement existing databased
SPEED Projectile and Mach Span

## Slide 17
Sample returns involve Earth re-entries that require robust TPS materials and understanding of air environments at high-velocity. Weave/GN&C development needs overlap with Outer Planets.
Mission Infusion: Sample Returns (Earth)
Launch to Landing GN&C
Coupled GNC (POST2) and trajectory (MONTE) solver provides insights to multiple mission concepts.
Fracture & Failure of Woven TPS
Developing models for TPS fracture and failure modes to improve reliability prediction and risk reduction for extreme entries.
Advancing Woven TPS Thermal Models
EM&I is developing woven TPS (e.g., HEEET) material models to quantify thermal uncertainties and aid design.
High-Speed Air Radiation
First of their kind databases for backshells and high velocity radiation have been developed. Radiation validated with shock tube data.
Mars Sample Return – Earth Entry System
Notes: Tom

## Slide 18: EM&I Stakeholder Capability Infusion
External Collaborators
EM&I collaborates extensively to accelerate capability development and infusion
Science, human exploration, and commercial space missions
30+ Major Academic Partners
Multiple NASA Centers and OGAS
NASA Project and Government Team
Spaceflight Projects and Missions
DLR (German Aerospace Center)
Ecole CentraleSupelec
Von Karman Institute
University of Queensland
Oxford University
Instituto Superior Tecnico
European Space Agency
JAXA (partnered with Orion)
Various International Partners

## Slide 19: Mission Infusion and Transition
 | Orion/Artemis | ESM: TPS Tools, Models, and Experiments for Char Loss Investigation ESM: Backshell radiative environment models and co-funded spectrometer Artemis I-III FTI: Spectrometer on SciFil for Artemis II imaging
 | Mars Sample Return Earth Entry System (EES) Sample Retrieval Lander (SRL) | ESM: Co-funded TPS material response models for woven TPS and TPS coatings ESM: Vehicle dynamic stability model development ESM: Aerothermal environments and multi-physics design tools FTI: SPEED data on capsule dynamic stability
 | Dragonfly | ESI: DrEAM providing EDL instrumentation for Dragonfly ESM: Multi-physics TPS design tools, Titan aerothermal environments ESM: Vehicle dynamics models development and co-funded ballistic range tests FTI: SPEED data on capsule dynamic stability
 | DAVINCI | ESI: VISTA providing EDL instrumentation for DAVINCI
 | SMD and HEO Futures: Ice Giants and Mars | ESM: Human-Mars will benefit from activities in all capability elements ESM: Uranus-Orbiter Probe aerothermal environments and TPS response
 | Commercial Space | ESM: ULA/Vera HIAD data products through LOFTID Deep Dive ESM: SpaceX and Blue Origin tool infusion for TPS design FTI: SciFli ACO SpaceX Starship Re-entry Observation FTI: SPEED Blue Origin Partnership on testing FTI: OSPREE ARFL Spectrometer Reconstruction from Varda flight
19

## Slide 20: Other Capabilities from EM&I Infused into Dragonfly
Benchmark Radiative Heating
The benchmark experimental data for Titan entry, along with validated models performed and developed within ESM
New Radiative Heating
New low density shock tube (LDST) online in the Electric Arc Shock Tube (EAST) at NASA Ames
Heatshield Coating Behavior
Improved models for behavior of NuSil coated Phenolic Impregnated Carbon Ablator (PICA)
Convective Cooling
Scale resolved convective cooling conducted to understand temperatures during descent
POCs: Brett Cruden, Aaron Brandis, Brody Bessire, Francois Cadieux
Capabilities have led to reduced radiative aeroheating baselines and margins – changing TPS sizing, mitigating heatshield thermostructural risk, and mitigating internal temperature exceedance risks