## Slide 1: Model Correlation and Thermal Analysis of xEMU Boot at Lunar South Pole Temperatures
Emma Quick, Amentum, Johnson Space Center
Noah Andersen, HX5 LLC, Johnson Space Center
Ben Swartout, Johnson Space Center
Shane McFarland, KBR HHPC, Johnson Space Center
ICES-2026-153
July 14, 2026
Trade names are used in this presentation for identification only. Their usage does not constitute an official endorsement, either expressed or implied, by the National Aeronautics and Space Administration.

## Slide 2: Contents
Background & Objectives
Test Setup/Conditions/Instrumentation
MiniShroud Model Overview
MiniShroud Model Correlation
Boot Model Overview
Boot Model Correlation
  Key adjustments, results, performance, RMSE
Lunar Operation
  Modeling, heat flux predictions, temperature predictions
Conclusions

## Slide 3: Background & Objectives
Upcoming Artemis missions will land astronauts on the moon at the south pole region
  Temperatures here can be as low as ~50 K
Exploration Extravehicular Mobility Unit (xEMU) boots will need to withstand these temperatures throughout extravehicular activity (EVA)
  Comprehensive thermal vacuum testing and subsequent thermal model correlation of the xEMU boot are essential to ensure crew safety
Test data was used to correlate the thermal model and predict lunar boot performance in permanently shadowed regions on the moon
An uncertainty analysis was also performed to quantify which model inputs have the highest uncertainty and impact on results

## Slide 4: Test Setup, Instrumentation, and Conditions
CITADEL TVAC chamber at NASA JPL
Thermal manikin foot outfitted with xEMU boot
  Water lines running through the foot maintain a skin boundary temperature
  Thermocouples/RTDs on various layers of the foot+boot stack-up
    56 external and 16 internal TCs
  Ventilation flow of 12.4 SLPM (1.5 ACFM) between the sock and bladder layers
  Pressurization of boot to 4.3 psia
MiniShroud for environmental temperature control
  Aluminum stomp pad for boot to contact
  Six environment TC coupons
Boot mounted on actuated push-rod system to simulate IVA to EVA transition
Test Parameters:
Variable Name | Levels | Units
Contact Pressure | 0, 40, 100 | lbf
Ventilation Flow | 0, 1.5 | ACFM
Foot Temperature | 28, 33 | C
Variable Name | Levels | Units
Contact Pressure | 0, 40, 100 | lbf
Ventilation Flow | 0, 1.5 | ACFM
Foot Temperature | 28, 33 | 

## Slide 5: MiniShroud Model
It was necessary to build the MiniShroud model instead of using single external sink node for the boot
  In test, the MiniShroud did not provide a cold, isothermal environment
Model built from JPL CAD and includes stomp pad, top/side/bottom panels, copper bars, Teflon stomp pad coverings, and SLI curtain
External MiniShroud environment simulated with sink temperature nodes on each face
G10 spacers on bottom of MiniShroud were not explicitly modeled, but represented with a gap and low-conductance contactor
Mechanical joints (screws, panel overlaps, interfaces) were modeled with face/edge contactors
  Conduction coefficients calculated based on screw count, conductivity, and contact area
Comparison of CAD file (.stp) and Thermal Desktop (TD) geometry. (a) CAD interior, (b) TD interior, (c) back of CAD, (d) back of TD.

## Slide 6: MiniShroud Model Correlation
The variables with highest uncertainty in the MiniShroud model were fed into Thermal Desktop SOLVER as design variables
  External environment sink temperatures, conductance from stomp pad to MiniShroud floor, conductance from bottom panels to the sides
Data from the test or from material specifications used as initial guesses in the model
SOLVER iterates until objective function is minimized. The object is defined as follows:
Where T represents temperatures at known TC locations on the walls of the MiniShroud
Optical and thermal properties were adjusted manually between iterations
Model was correlated to 4 steady state radiation and contact test points separately since the temperature of the stomp pad affects the wall temperatures

## Slide 7: MiniShroud Model Correlation Results
Design Variable | All Radiation Test Points | Contact, 48-60 K setpoint | Contact, 100 K setpoint | Units
Tchambersink_floor | 255.8 | 272.0 | 264.2 | K
Tchambersink_left | 284.9 | 279.8 | 282.9 | K
Tchambersink_right | 255.4 | 255.4 | 255.4 | K
Tchambersink_top | 309.1 | 289.2 | 299.2 | K
Tload | 292.0 | 294.8 | 294.7 | K
StompPad2Bottom | 16.139 | 21.276 | 25.297 | W/K/m2
Flap2SideScrew | 0.100 | 0.129 | 0.100 | W/K

## Slide 8: Boot Model
EPG regions had adjustable effective emissivity for tuning purposes
Stomp contact could be modeled with just the tread tops (hard flat surface) or the entire outsole (granular regolith)
Thermal Desktop Boot Model: (a) sock, (b) pressure bladder, (c) restraint layer, (d) frame, (e) thermal insert, (f) outsole, and (g) full assembly. Magenta regions represent TC locations.
Built from CAD of xEMU boot model
Layer material properties such as conductivity, specific heat, and optical characteristics match actual hardware
Foot is represented with boundary nodes to match manikin’s isothermal behavior
  Full human foot model not available
Linear conductors and contacts capture internal heat transfer paths
External heat transfer paths include radiation and outsole conduction

## Slide 9: Boot Model Correlation
The variables with highest uncertainty in the MiniShroud model were fed into Thermal Desktop SOLVER as design variables; sensitivity analysis performed to determine design variables
  Thermal contactors/conductors between boot layers, thermal and optical properties, and insulation performance
Data from the test (calculated conductances) used as initial guesses in the model
SOLVER iterates until objective function is minimized. The object is defined as follows:
Where T represents temperatures at known TC locations on the boot and q represents the heat leak out of the boot
Optical and thermal properties were adjusted manually between iterations
Model was correlated to contact and radiation cases separately
Foot to sock conductance was allowed to vary between flow and no flow cases

## Slide 10: Key Adjustment to Boot Model
The effective emissivity of the EPG increased from 0.06 to 0.10 to correct excessive predicted heat loss through the sole
  Justified by the complex geometry of coverage and layer compression effects
The thermal insert conductivity was decreased by an order of magnitude
  Accounts for combined effects of geometry, material properties, multi-layer insulation (MLI) distribution, and dimple contact on heat transfer
The stomp pad emissivity was increased from 0.2 to 0.5 to correct overly warm outsole temperature predictions
  Supported by the Teflon layers (emissivity ~0.9) covering most of the stomp pad surface
The contactors between the pressure bladder and restraint were adjusted to represent a toe that does not have perfect contact with the toe of the boot
  In contact cases, the restraint and bladder in the toe regions were consistently colder in test than predicted by the model, likely due to a higher resistance from the toes to the pressure bladder and restraint
Outsole-to-stomp pad conduction was allowed to vary between contact cases to align with TC data
  Supported by probable inconsistency or nonuniform contact with the stomp pad from case to case

## Slide 11: Boot Model Correlation Results
In general, the model is slightly conservative for contact cases (overpredicting heat leak) and slightly non-conservative for radiation-only test points.

## Slide 12: Boot Model Thermal Performance
Radiation case temperature gradients throughout individual layers of the boot. (a) sock, (b) pressure bladder, (c) restraint, (d) frame. Temperature in Celsius are provided in parentheses.
Radiation case temperature gradients between layers of the boot. (a) restraint, frame, and thermal insert; (b) outsole. Temperatures in Celsius are provided in parentheses.

## Slide 13: Boot Model Predictions (RMSE)
Analysis showed that sensors closest to the foot exhibit the lowest error, while sensors near the outsole and EPG have higher variability due to large thermal gradients and positional uncertainty.
Heat leak predictions were highly accurate which can be attributed to the deliberate modeling strategy of prioritizing the heat loss correlation accuracy
Location | Expected (W) | Uncertainty on (W)
Bottom of Foot | 0.101 | +0.042 / -0.033
Top of Foot | 0.076 | +0.021 / -0.018
Location |  | 
Bottom of Foot | 0.101 | +0.042 / -0.033
Top of Foot | 0.076 | +0.021 / -0.018

## Slide 14: Lunar Operation Modeling
Gaps identified for accurate representation of lunar operation
  Unknown outsole-to-regolith thermal conductance
  Lack of high-fidelity metabolic foot model
  No dynamic gait modeling such as flexion and compression
Updates to model:
  Outsole contact increased to include tread valleys that would be filled by granular regolith
  Initial conductance assumed came from test-derived outsole-to-stomp pad value of 2.703 W/m2K
  Foot represented with the upper and lower nodes as well as a new third node representing the toes, since this area was colder throughout testing
Permissible Heat Flux Criteria:
  Used to assess safety since model does not resolve detailed foot anatomy
  Limits derived from EMU glove testing which used high-fidelity metabolic hand model
    Thumb tip used as analog for toe heat flux requirement
  Skin temperature thresholds were identified and the heat flux leaving the test article that resulted in the skin temperature hitting that threshold was calculated
    10C (50F) threshold →120.8 W/m2 heat flux
    15C (59F) threshold → 111.4 W/m2 heat flux

## Slide 15: Lunar Operation Heat Flux Predictions
Heat flux at the toe was evaluated for varying environment temperatures between 48 K and 120 K and outsole-to-regolith contact conduction between 0.24 Btu/hr/ft2/°F (1.36 W/m2/K) and 159.2 Btu/hr/ft2/°F (904 W/m2/K), assuming foot temperatures of 10 °C (50 °F) and 15 °C (59 °F), such that the heat leak calculated would model the heat leaving the toes when the skin temperature limit is reached.
Results are highly dependent on the sole to regolith contact conductance, impacting pass/fail outcome
Error bars represent the standard error for the model, as computer using a Monte Carlo Simulation.
When applying a 10 °C skin temperature limit, the boot is likely safe for 8‑hour operation down to ~100 K, but performance at 48 K is inconclusive (and not feasible for any conductance at the stricter 15 °C limit), with exposure limits at 48 K requiring transient analysis that the current model cannot provide.

## Slide 16: Lunar Operation Temperature Predictions
Layer | Minimum Permissible Temperature | Minimum Expected Temperature at 48 K (with 95% confidence) | Minimum Expected Temperature at 100 K (with 95% confidence)
Bladder | -34.4 °C | -37.2 to -5.0 °C | -34.0 to -3.3 °C
Upper Frame | N/A | -109.0 to -37.0 °C | -96.6 to -30.2 °C
Outsole | N/A | -225.2 to -157.7 °C | -173.2 to -126.4 °C
Assumes a constant foot temperature of 10 °C
Addresses outsole-to-regolith contact conductance uncertainty and inherent model uncertainty
Derived from contact conductance range of 0.24 Btu/hr/ft2/F to 159.2 Btu/hr/ft2/F
Model uncertainty incorporated by adding RMSE error to this range, 2 times RMSE yields a 95% confidence interval
Temperature ranges for all layers large
  Due to uncertainty in contact conductance
  Methods for reducing ranges:
    Additional testing to better characterize outsole-to-regolith conductance
    Refinement of model correlation with emphasis on specific temperatures
    Narrowing confidence interval

## Slide 17: Conclusions
Successfully correlated lunar boot thermal model using extensive, repeatable steady-state data obtained across 10 test points including contact and radiation cases
  Achieved heat leak accuracy within 0.1 W
Used bootstrapping and Monte Carlo methods to quantify model uncertainty for both test and operational conditions
Outsole-to-regolith contact conductance identified as the dominant driver of heat flux and temperature variability
  Bounded its impact and defined permissible environmental temperatures with parametric studies
Future improvements needed in regolith contact fidelity, colder/more uniform radiation environments, and human in the loop testing to validate a high-fidelity metabolic, transient, foot model

## Slide 18: References
[1] | B. Swartout, "xEMU Spacesuit Boot Lunar South Pole Thermal Vacuum Testing," in International Conference of Environmental System, Rio Grande, Puerto Rico, 2026.
[2] | B. Swartout, "Exploration Extravehicular Mobility Unit (xEMU) Lunar Boot Chamber B Thermal Vacuum Testing Results," in International Conference on Environmental Systems, Louisville, 2024.
[3] | B. C. Conger, "Thermal Analysis of the EMU Boot with Foam Insert Removed," CTSD 1404, 1992.
[4] | T. Durrant, "Orlan Spacesuit Boot Thermal Model," HDID-2G41-1132, 1999.
[5] | J. V. Iovine, "EMU Boot Thermal Analysis for ISS EVA," HDID-2G41-954, 1998.
[6] | J. V. Iovine, "Thermal Analysis of the EMU Boot Pressure Bladder," CTSD862, 1990.
[7] | W. Lee, "Thermal Analysis Results of Stand-Alone Shuttle Boot Model for the Thermal Vacuum Chamber B Test for STS-37 Mission Hardware," CTSD454, 1989.
[8] | T. Nguyen, "The Thermal Effect of a Newly Designed Aluminum Piece Attached to the Heel of the EMU Boot," 20977, 1984.
[9] | D. Ochoa, "Thermal Design and Analysis of Constellation Space Suit System Boot Options for Lunar Missions," ESCG-4470-09-TEAN-DOC-0110, 2009.
[10] | D. G. Gilmore, Spacecraft Thermal Control Handbook: Volume 1: Fundamental Technologies, The Aerospace Press, 2002.
[11] | "fitgeotrans," Mathworks, [Online]. Available: https://www.mathworks.com/help/images/ref/fitgeotrans.html.
[12] | "imwarp," Mathworks, [Online]. Available: https://www.mathworks.com/help/images/ref/imwarp.html.
[13] | Z. Fester, S. McFarland, N. Andersen, E. Quick, D. Green, T. Jaimes and D. Morris, "xEMU Boot TVAC Final Report," NASA, CTSD-ADV-2272.
[14] | N. L. Langston and V. Margiott, "EMU Phase VI Glove Thermal Vacuum Test and Analysis Final Report," CTSD-SS-1621, 1998.
[15] | M. B. Abney, R. J. Jones, S. R. Wilson, T. K. Brady and N. L. Andersen, "Lunar Glove Thermal and Durability Analysis, Test, and Failure Mitigation," NESC-RP-21-01722, 2024.
[16] | NASA, "NASA Spaceflight Human-System Standard Volume 1, Crew Health," 2023.

## Slide 19: Acknowledgements / Questions
The authors would like to acknowledge the CITADEL test team at JPL for their hard work conducting test points and compiling data files.
Thank you!
Questions?
Further inquiries may be sent to the following:
Emma Quick: emma.j.quick@nasa.gov
Noah Andersen: noah.l.andersen@nasa.gov