## Slide 1
Acknowledgement: The co-authors would like to acknowledge the HWO Technology Maturation Project Systems Engineering Team for their significant contribution to the EACs design, modeling, and analysis work.
Habitable Worlds Observatory,
Exploratory Analytic Cases Formulation and Analysis
Alice Liua, James Governb, Josh Abela, Jordan Effrona, Jon Lawrencea, Marie Levinec, Charley Noeckerc, Kenneth Dziakb, Gary Kuanc, Alan Gostina, Joseph Howarda, Cameron Haagc, Connor Mulrenina, Breann Sitarskia, J. Scott Smitha, Gregory Walsha, John Ziemerc
NASA’s next flagship mission,
recommended by the Astro2020 Decadal Survey
Large Aperture UV/Optical/NIR observatory performing transformative astrophysics across cosmic time
First telescope designed to directly image and characterize Earth-like exoplanets, including search for signs of life
HWO IM Analysis Pipeline
The first 3 EACs examined a wide range of trade options spanning science, mission system, observatory, payload, and spacecraft, with some trades continuing to future EAC iterations
Architecture Trade Options
SC-to-Payload Vibration Mitigation System (SPVM)
SC-to-Payload Vibration Mitigation System (SPVM)
Spacecraft Element
Spacecraft Bus
ACS Hardware, Propulsion
Avionics, Comm, C&DH, FSW, Power System
Solar Arrays
Sun-Shade or Instrument Radiator Shields
Deployable Baffle System
DBS Containment Box
Deployable Baffle
Optical Telescope Element
Primary Mirror (PM) Segments
PM Backplane
Assembly (PMBA)
Secondary Mirror Assembly (SMA)
Secondary Mirror Support Structure
Instrument and Guider Element
Instrument 1
Extra Instrument (XI)
Instrument Radiator Assemblies (Multiple radiators)
Instrument Module Structure
Instrument 2
Instrument 3



IMS Door (Launch Support)
Observatory Element Schematic
Building on JWST and Roman heritage, HWO is leveraging Integrated Modeling, a multidisciplinary analysis used to predict system performance, to quickly bridge design exploration and end-to-end engineering and science performance metrics
EAC-1
EAC-2
EAC-3
Single Baseline for MCR
EAC-4
EAC-5
Explore  Design  Analyze  Repeat
EAC-6
Additional Designs
(Government and Industry D.19 Studies)
EAC-4 Objectives
Balance cost, schedule, risk and science
Maximize aperture diameter while reducing baffle and PM deployment complexity​
Mitigate baffle-related engineering risks​
EAC-5 Objectives
Driven by science goals with realistic launch vehicle constraints and technological advances
Minimum 8-m inscribed diameter aperture
Consider large flat sunshade
Includes mass and design margin
Mission architectures developed to explore the HWO trade space:
Explore key architectural options and breakpoints to guide future point design decisions
Develop end-to-end models and tools to understand modeling capabilities and needs
Identify technology gaps and guide maturation of potential solutions
Provide early feedback to launch vehicle vendors to help influence their direction
Exploratory Analytic Cases (EAC)
Segmented primary mirror and coronagraph instrument
Orbit at Sun-Earth L2 with a serviceable architecture
Baffle/barrel protection against micrometeoroid impacts
Compatible with at least two future launchers
Field-of-Regard: ±45° pitch, ±22.5° roll, 360° yaw
Slew/Settle: 90° in 60 min
Observatory LOS stability: 4 mas
Passive cooling for NIR detectors
ULE glass mirrors (primary/secondary)
at room temperature for simplified I&T
EAC Design Guidelines
EACs 1-3 Key Findings
Deployable baffle poses significant engineering challenges, requiring thermal stability, MMOD protection, and solar heat rejection while stowable in fairing volume and deployable on-orbit
Solar arrays limit radiator heat rejection options; The coronagraph requires optimal cold space view factors to achieve passive detector cooling
Primary mirror thermal environment directly drives optical performance and active control system complexity
The large CP-CM offset (>1 m) creates significant attitude control challenges, driving high propellant consumption and complex thruster placement requirements
Key serviceability challenges include maintaining picometer-level latch stability during instrument exchanges, robotic cryogenic heat strap connections, and structural access constraints from the primary launch structure
EAC-1
6m ID / 7.2 m OD off-axis PM
19 hex segments
PM faces horizontal in rocket
JWST-like wing deployment
EAC-2
6m ID (round) off-axis PM
Central 3 m round mirror +6 keystone
PM faces up in rocket
Non-deployed PM
EAC-3
8m ID (round) off-axis PM
34 keystone segments
PM faces horizontal in rocket
JWST-like wing deployment
Initial EACs
UV/Vis multi-object spectroscopy and FUV imaging | 
Bandpass | ~100–700 nm
Field-of-View | ~
Apertures | ~
 | ~500 & 50,000
UV/Vis multi-object spectroscopy and FUV imaging | 
Bandpass | ~100–700 nm
Field-of-View | 
Apertures | 
 | ~500 & 50,000
UV/Vis and NIR imaging | 
Bandpass | ~200–2500 nm
Science FoV | ~
Astrometry FoV | ~12 sq. arcmin
~40 science filters & grism | 
UV/Vis and NIR imaging | 
Bandpass | ~200–2500 nm
Science FoV | 
Astrometry FoV | ~12 sq. arcmin
~40 science filters & grism | 
High-contrast imaging and imaging spectroscopy | 
Bandpass | ~450–1700 nm
Contrast | 
 | Vis: ~140, NIR: ~70
High-contrast imaging and imaging spectroscopy | 
Bandpass | ~450–1700 nm
Contrast | 
 | Vis: ~140, NIR: ~70
Diameter | ≳6.0 m
Bandpass | ~100–2500 nm
Diff. Limit | ~500 nm
Telescope
Coronagraph
High-Resolution Imager
UV Multi-Object Spectrograph
aNASA Goddard Space Flight Center, 8800 Greenbelt Rd., Greenbelt, MD, 20771 USA
bAerodyne Industries, 8910 Astronaut Blvd., Suite 208, Cape Canaveral, FL, 32920 USA
cJet Propulsion Laboratory, California Institute of Technology, 4800 Oak Grove Dr., La Cañada Flintridge