## Slide 1: Development of the METMAN Thermal Desktop Human Model for System Integration
Ellie Thurston
NASA Johnson Space Center
Crew and Thermal Systems Division
EC2: Design and Analysis Branch
55th International Conference on Environmental Systems
12-16 July 2026, Rio Grande, Puerto Rico
Human Health and Performance Analysis ICES-513A-465
Trade names and trademarks and company names are used in this report for identification only. Their usage does not constitute an official endorsement, either expressed or implied, by the National Aeronautics and Space Administration.

## Slide 2: Introduction
Human Thermal Modeling (HTM) and vehicle thermal modeling provide comprehensive simulations of extreme mission environments
Human and environmental/vehicle models have historically been decoupled1
This presentation describes the development of METMAN TD, an updated format of the NASA METMAN human model for 3D coupling with vehicle/thermal systems
Introduction
Background
Model Overview
Results
Conclusion
Diagram of Thermal Model Information Exchange between METMAN2 and Orion Vehicle Model

## Slide 3: Introduction to Human Thermoregulation
Introduction
Background
Model Overview
Results
Conclusion
Human Thermal Modeling (HTM) characterizes the heat transfer between a person and the environment
Goal of the thermoregulatory system: maintain homeostasis of the core body temperature
Passive System4: fixed parameters
  Anthropometry
  Gender*
  Tissue composition
Active System4: thermoregulation
  Sweating
  Shivering
  Blood flow
Diagram of Passive and Active Human Thermoregulation3

## Slide 4: Overview of the METMAN Model
Introduction
Background
Model Overview
Results
Conclusion
METMAN: the NASA human thermal computational model (Fortran)
  Initially developed in the 1970’s for use on Apollo systems1
  Current use cases involve EMU, ISS, Orion
Human body segments are represented as layered, concentric cylinders
Model subroutines break down the different functions of thermoregulation
Model is a standalone tool, leading to iterative analysis for dynamic environments
Diagram of METMAN Segment and Layer Distribution2

## Slide 5: Transition in HTM Utilization
Introduction
Background
Model Overview
Results
Conclusion
NASA HTM tools were originally developed for specific use-cases; the discipline has evolved to support multiple programs and systems
Human models are “stand-alone” tools; implementation becomes challenging with varied interfaces
As thermal architectures become more complex, there is a growing need to couple the thermal exchange between humans and environmental systems
Thermal Desktop chosen as the model format to facilitate integration within the standard analysis software
Designed for Apollo era systems
Needed for versatile use cases

## Slide 6: Modeling Process: High Level Structure
Introduction
Background
Model Overview
Results
Conclusion
Create geometry framework for Passive System
Modularize Fortran Code into Submodel Logic Blocks
Connect logic code to graphical nodes and conductors
Modeling process: break down the METMAN Passive System and Active System into modules.
3D cylindrical TD objects
“Skin layer” used for environmental interface
METMAN thermal subroutines contained in TD logic objects
Heat loads stored as SINDA Registers and applied to TD nodes
“Schematic” connects thermal logic to graphical nodes
Skin nodes cloned to passive system

## Slide 7: Components of Human Thermoregulation
Introduction
Background
Model Overview
Results
Conclusion
+QMET
+QCOND (to layer)
-QCOND (from layer)
-QLAT
-QSENS
-QRAD
-QCONV
Heat Storage5: heat in – heat out
Modes of Heat Transfer:
  QMET: Metabolic heat production rate (muscle work + shiver)
  QCOND: Cylindrical conduction between layers
  QSENS: Sensible heat transfer to the environment (convection and respiration)
  QRAD: Radiation to environment
  QLAT: Heat rejection from sweating, diffusion, and respiration
  QCONV: Internal convection (blood flow)
Layer Dependent: each layer has its own heat balance that contributes to overall body temperature

## Slide 8: Thermal Control of the Passive System
Introduction
Background
Model Overview
Results
Conclusion
Internal conduction transfers heat between tissue layers per body segment
Thermal capacitance is the product of body compartment weight and specific heat
  Determines individual node temperature increase/decrease depending on total heat load2
Active system regulates temperatures to mitigate thermal stress
2

## Slide 9: Heat Production in the Body
Introduction
Background
Model Overview
Results
Conclusion
Basal metabolic rate: baseline rate of metabolic heat generation to maintain essential life functions2
  Biochemical processes + muscle activity produces heat to be dissipated to the environment
Heat generation through shivering:
  Shiver distribution is allocated proportionally2
  Segment shivering is enabled if:
    Full body: Core temperature < setpoint
    Per segment: Skin temperature deviance from setpoint is negative

## Slide 10: Sensible Heat Transfer
Introduction
Background
Model Overview
Results
Conclusion
Calculation of both free and forced convection
  Driven by temperature differentials, G, and air flow
Radiation: Heat emitted to surrounding environment
Respiration: Cool air enters the body and warmed by convection
  Driven by respiratory temp and met rate
Inhale
Exhale
Cool air
Warm air
Respiratory Tract Temp
Convection
Radiation

## Slide 11: Latent Heat Transfer
Introduction
Background
Model Overview
Results
Conclusion
Latent heat transfer: dissipation of heat through phase change
Diffusion: vapor pressure differences cause latent heat loss
Respiration: dry gas flow over moist respiratory tract
Sweat: evaporation of sweat cools the skin

## Slide 12: Internal Convection: Blood Flow
Introduction
Background
Model Overview
Results
Conclusion
Internal Convection: the heat exchange between flowing blood and each respective segment
Basal Blood Flow: flow needed to maintain baseline metabolic requirements
Muscle Work: more blood flow needed during elevated metabolic rates
Vasoconstriction: decreased flow rate to conserve heat
Vasodilation: increased flow rate to reject heat

## Slide 13: Applying the Total Heat Balance
Introduction
Background
Model Overview
Results
Conclusion
Node = 1
41
Head
L Arm
L Hand
L Foot
L Leg
R Foot
R Leg
Torso
R Hand
R Arm

## Slide 14: Model Results: Constant Metabolic Rate
Introduction
Background
Model Overview
Results
Conclusion
Comparison between METMAN code and METMAN TD shows near identical agreement
Steady State example: Metabolic rate held constant at 474 BTU/hr, ambient environment held constant at 85°F
Temperatures at each node match Fortran outputs

## Slide 15: Model Results: Transient Metabolic Profile
Introduction
Background
Model Overview
Results
Conclusion
Results verification: Model outputs were compared against METMAN analysis of exercise environment: showed almost identical agreement
METMAN is correlated to human test data: METMAN TD provides a firm foundation for human thermal model evolution and can be used for existing systems with embedded METMAN requirements
METMAN TD Transient Analysis of Core Temperature at Varied Metabolic Profile

## Slide 16: Added Capabilities of a TD Interface
Introduction
Background
Model Overview
Results
Conclusion
Can increase fidelity as needed
METMAN functionality in a modernized format
Graphical components to interface with vehicle and thermal system models
Modularized structure enables evolution alongside systems and mission contexts
Next steps: Integrate METMAN TD with inline analysis work, such as Artemis II post-flight thermal comfort studies
Baseline METMAN: Symbol driven inputs
Customizability for advanced use-cases

## Slide 17: Acknowledgements
This work was supported by the NESC ECLSS Technical Discipline Team (TDT) as a discipline-advancing effort. The human thermal analysis team would like to thank Morgan Abney, Thomas Chen, and the rest of the NESC ECLSS TDT for their support on this model development effort.
Introduction
Background
Model Overview
Results
Conclusion
Thank you!

## Slide 18: Thank you!
Questions?

## Slide 19: References
[1] H. J. Song, Overview of Human Thermal Modeling, Thermoregulation, and Thermal Comfort at NASA, NASA, 2017.
[2] G. C. Bue, "Computer Program Documentation 41-Node Transient Metabolic Man Program," LESC-27578, CTSD-0425, 1989.
[3] M. Haas and D. J. Hartl, "Development of a Three-Dimensional Scripted Human Thermoregulation Model Framework for the Lower Limb," in 53rd International Conference on Environmental Systems, Louisville, Kentucky, ICES-2024.
[4] D. Fiala, K. J. Lomas, M. Stohrer, "A Computer Model of Human Thermoregulation for a Wide Range of Environmental Conditions: the Passive System," Journal of Applied Physiology, vol. 87, no. 5, 1999.
[5] J. A. J. Stolwijk, "A Mathematical Model of Physiological Temperature Regulation in Man," NASA CR-1855, 1971.
Additional references found in accompanying paper:
"Man-Systems Integration Standards," NASA-STD-3000, 1995.
"NASA-STD-3001_VOL_2," NASA, 2025.
"Human Integration Design Handbook (HIDH)," NASA, 2014.
"Constellation Program Human-Systems Integration Requirements," NASA, 2010.
M. Ewert, T. T. Chen, C. D. Powell, "Life Support Baseline Values and Assumptions Document," NASA, 2022.
"Gateway System Requirements," NASA-DSG-RQMT-001, 2019.
M. Ewert, M. E. Downs, J. F. Keener, "Developing a Daily Metabolic Rate Profile for Human Exploration Missions," in 50th International Conference on Environmental Systems, 2021.
T. Golubev, M. Hepokoski, M. Klein, A. Curran, H. J. Song, "Validation of a Human Thermal Model for Assessing Crew-Induced Loads in Spacecraft," in 51st International Converence on Environmental Systems, St. Paul, Minnesota, 2022.
D. DuBois, E. F. DuBois, "The Measurement of Surface Area of Man," Archives of Internal Medicine, vol. 15, pp. 868-888, 1915.
J. A. J. Stolwijk, J. D. Hardy, "Temperature Regulation in Man," Pfluger Archiv ges. Physiologie, vol. 291, pp. 129-162, 1966.
Introduction
Background
Model Overview
Results
Conclusion