## Slide 1: NASA Space Launch System Artemis I & II Post Flight Ascent Aerothermal Environments Overview
Brandon L. Mobley NASA MSFC, Aerothermodynamics Team Lead, Huntsville, Alabama Samantha Summers NASA MSFC, GeoControl Systems, Huntsville, AL
Thermal & Fluids Analysis Workshop TFAWS 2026 August 31 – September 4, 2026
NASA Marshall Space Flight Center
Huntsville, AL
TFAWS Aerothermal Paper Session

## Slide 2: Notice to the Audience
The Space Launch System, including its performance and certain other features and characteristics, have been defined by the U.S. Government to be Controlled Unclassified Information (CUI). Information deemed to be CUI requires special protection and may not be disclosed to an international audience. To comply with CUI restrictions, details such as absolute values have been removed from plots and figures. It is the opinion of the authors that, despite these alterations, there is no loss of meaningful technical content. Analytical methodologies and capabilities are discussed, technical results and trends are presented, conclusions are captured.

## Slide 3: Introduction
MSFC EV33 Aerothermodynamics Team over the last 30 years has been using the MINIVER (CLVMIN400) aerodynamic heating and aerothermal environment integration (CLVINT 304) with engineering plume codes, CFD and scale model data, to develop ascent aerothermal design environments:
  Design Environments (pressure & heat transfer): one-way coupled, integrated components of external heat transfer (convection provided at varying wall temperature) to be used as external boundary conditions to thermal models
  Aerodynamic Heating Engineering Code: provides a foundation to model both the isotropic inertial flow field (edge conditions) and inner viscous, boundary layer regions, heating predictions using heating relationships (e.g. Reynolds analogy, similarity transformations) used in conjunction with existing wind tunnel, CFD or Developmental Flight Instrumentation (DFI) data to determine heat flux at the surface point
  Plume Induced Environments (radiation and convection): predicted separately, independent database, radiation is summed with either plume or aerodynamic convection
  Monte Carlo capability to account for trajectory variation to provide a statistical range of environments with respect to peak heat load, or peak heat rate over the trajectory

## Slide 4: Introduction
Artemis II consisted of 3183 body point models, 75 co-located with DFI
Flight instrumentation was selected to:
  Substantiate models, reduce uncertainty, observe total heating margins
  Observe cardinal flow field characteristics
Six flight objectives, assessing model performance from six unique sources:
  Aerodynamic Heating
  Base Plume Induced Radiation
  Base Plume Induced Convection
  Direct Plume Impingement
  Plume Induced Flow Separation
  Core Auxiliary Power Unit Plumes

## Slide 5: AR02 Aerothermal Instrumentation Summary
Orion Multi-Purpose Crew Vehicle (MPCV)
  5 Calorimeters with embedded sensor thermocouples
  5 Static pressure gauges
Integrated Spacecraft and Payload Element (ISPE)
  3 Calorimeters with embedded sensor thermocouples
  3 Static pressure gauges
Core Stage (CS)
  38 Calorimeters with embedded sensor thermocouples
  27 Static pressure gauges
  8 Radiometers
  7 Gas temperature probes
Core Stage Engines
  None (Engine #4 Swap), AR01
Solid Rocket Booster (SRB)
  24 Calorimeters with embedded sensor thermocouples
  24 Static pressure gauges
  4 Radiometers
  3 Gas Temperature Probes
  2 Flow direction probes

## Slide 6: AR02 Aerothermal Instrumentation Summary
Aerodynamic Heating & BSM Plume Impingement Island
  Medtherm Model 20850 Schmidt-Boelter Calorimeter with Embedded Thermocouple (50Hz)
  Kulite Model LLE-17DC-500 Pressure Transducer (500Hz)
Calorimeter
Pressure Transducer
Left Booster Separation Motors

## Slide 7: AR02 Aerothermal Instrumentation Summary
Center Base Heat Shield DFI
  Medtherm Model 20850, Schmidt-Boelter Calorimeter with Embedded Thermocouple (50Hz)
  Medtherm Model 22121, Radiometer with Sapphire Window (50Hz, 150 deg FOV)
  Medtherm Model 11290, Base Gas Temperature Probe, (50Hz)
  Kulite Model LLE-17DC-500 Pressure Transducer (500Hz)
Calorimeter
Pressure Transducer
Radiometer
Gas Temperature Probe

## Slide 8: Artemis II Aerodynamic Heating

## Slide 9: Aerodynamic Heating
One major difference between Artemis I to Artemis II aerodynamic heating was the additions of aerodynamic strakes which lead to increases in aerodynamic heating in the forward booster attach regions on the Core Stage and Booster
  A strake is a thin, fin-like structure commonly improve unsteady airflow and stability
  Adding them to the Core Stage changed the induced acoustic frequency and spatial distribution, reducing the maximum potential structural response
  Strake constraint results in increased total pressure in capture area, increasing heat transfer coefficient, aerodynamic heating
Source: https://www.nasa.gov/directorates/esdmd/common-exploration-systems-development-division/space-launch-system/from-supercomputers-to-wind-tunnels-nasas-road-to-artemis-ii/

## Slide 10: Artemis I & II Core Stage Aerodynamic Heat Flux Contours
AR02 CFD (2026) M∞= 3.5
AR01 CFD (2023) M∞= 3.5
2023, 2026 Loci-CHEM CFD Solutions, Single Species Air, Menter’s Baseline Turbulence Model
CFD Contour plots Courtesy of Matt Slaby

## Slide 11: Strake Aerothermal Impacts
Visible Charring

## Slide 12: Artemis II PLUME INDUCED HEating

## Slide 13: AR02 Evolution of Base Heat Shield TPS Pyrolysis, Burning

## Slide 14: AR01 vs. AR02 Base Plume Radiation
Similar radiation levels between flights
Heavy “belch” of BHS soot drastically clouds radiometers as evidenced in radiometer response, radiometers may coated with combustion products
AR02 used AR01 GASRAD-RMC plume radiation models with attenuation factors
Fire unsustainable without induced radiation

## Slide 15: SRBs are impacted by Core Base Burning
SRB Nozzle and CS Engine Configuration is unique to SLS
  Booster aft skirt is downstream of CS base heat shield
Flight Observations:
  Inboard regions experienced effects from CS base burning

## Slide 16: Plume Induced Base Environment Summary
Transition
Fully Recirculating
Cork Combustion
Choke Flow
Base Environment Summary
Similar Transition Altitude, Aspirating to Recirculating Flow, SRB Shutdown
Central RS-25 plume recirculation engulfs center base region, outboard env driven by RS-25-SRB plume interaction
Flight-to-flight Variability
Base Heat Shield TPS Burn Onset
Spatial distribution, heating magnitudes
Booster Shutdown
Booster Separation
Time
Booster Influence
RS-25 Influence

## Slide 17: Plume Induced Flow Separation Heating
Total Heat Flux
Booster-RS-25 Interaction
Center Base PIFS

## Slide 18: Plume Impingement Heating
Booster Separation & Launch Abort System Jettison Motor (BSM, LAS JM)
Plume Impingement
Max heat rates, local to nozzle exits
BSM plumes induced flow separation, progressed up to Orion ogive
Post AR01 CFD predictions based upon dispersed, jet po/p ratio, dynamic pressure
CFD Movie Courtesy of Josh Wilson/MSFC EV33
CFD Mach Contours

## Slide 19: Core Auxiliary Power Unit Plume Environments
CAPUs power RS-25 operations initially using pressurized He, before turning over to GH2, operate at high and low mass flow rates
Free H2 plume is disposed in base, combustion with entrained air in likeness to a diffusion flame
CAPU H2 (Low Flow Rate)
CAPU H2 (High Flow Rate)
IR Imagery courtesy of Darrell Gaddy/ER43
CAPU Plot, M.Mehta
CAPU Ports
TOT031

## Slide 20: Conclusions
Aerodynamic heating strongly influenced by the recovery of total pressure in the booster nose, frustum, capture area, the local heat transfer coefficient increased when adding further flow constraint with strakes
TPS burning induced environments sensitive to plume induced entrainment of free oxygen, material pyrolysis characteristics, off-gas products and radiation view factors, be aware of further consequences of TPS ablators
In addition to plume radiation, CAPU free H2 combustion contributed to base heating leading up to TPS combustion
Two-phase SRB plume induced environments, recirculation and radiation most challenging plume models with plume interactions
While BSM and LAS jettison motor plumes separated the freestream flow, there was less evidence of the turning of plume gases downstream impacting greater extent of heating on Core Stage, max rates were very local due to relatively short burn times

## Slide 21: References
NASA, “Space Launch System: Reference Guide for Artemis II”, released October 2025.
Mobley, B., Summers, S. (2024), “Validation of Artemis I Aerothermal Design Models using Developmental Flight Instrumentation”, NASA Thermal & Fluids Analysis Workshop, (TFAWS2024-AE-2).
Morris, C.I. (2015), "Space Launch System Ascent Aerothermal Environments Methodology", 53rd AIAA Aerospace Sciences Meeting, AIAA SciTech, (AIAA 2015-0561), Kissimmee, FL.
Mehta, M., Mobley, B., Smith, S.D. (2024), “Space Launch System Base Aerothermodynamics Post-Flight Reconstruction for Artemis I”, AIAA SCITECH 2024 Forum, (AIAA 2024-0256), Kissimmee, FL.