## Slide 1: SR-1 Freedom Thermal Architecture Challenges
Scott Thomas | NASA/MSFC
Jared Berg | NASA/GRC
Thermal & Fluids Analysis Workshop TFAWS 2026 August 31 – September 4, 2026
NASA Marshall Space Flight Center
Huntsville, AL
TFAWS Passive Thermal Paper Session

## Slide 2: Agenda
What is SR-1 Freedom?
Thermal Architecture Overview
Integrated Thermal Analysis Approach
Nuclear Power Module (NPM)
Heat Rejection System (HRS)
Thermal system challenges

## Slide 3: What is SR-1 Freedom
SR-1 Freedom seeks to advance U.S. space fission system technologies that will enable power generation capabilities in-space, on the Moon and Mars.
Goals and Objectives:
  Operate a nuclear-electric propulsion system in space
  Launch on Earth escape trajectory
  Utilize the 2028 Mars launch period
  Leverage existing technology and flight hardware to the maximum extent possible
  Deliver Skyfall to Mars Intercept
  Reactor Extended Performance
  Fly by Mars with imagery return
Re-purposes the Power and Propulsion Element (PPE), previously developed for Gateway
Target Launch Date: December 2028
Credit: NASA
Credit: NASA/JPL-Caltech

## Slide 4: SR-1 Thermal Architecture
Primary Heat Rejection to Space
2 Wings of 3 Radiator Panel Arrays
7m2 per panel side  84m2 total area
Average Trad ≈ 400K (260F)
2 pumped fluid loops – 1 per wing
Heat values shown are notional/approx.
PPE
Brayton
HRS
2 Wings
PLR
SKYFALL
BOOM
20kWe Power Delivered to PPE
Excess Power Converted to Heat and Rejected to Space
20kW
120kW
100kW
PPE Heat Rejection
Skyfall Heat Rejection
80kW
Reactor Total Thermal Load
Heat Transferred to Brayton Engine
Heat Loss to Space
Heat Loss to BOOM
ROSA
PPE Radiators

## Slide 5: Integrated Thermal Analysis Approach
Integrated Thermal Analysis centers around developing and maintaining the SR-1 Integrated Thermal model (ITM), consisting of Reduced Thermal Models (RTMs) for all Spacecraft Elements
  The ITM is used by other Spacecraft Elements for their detailed thermal analysis (similar process used for Gateway)
Due to project schedule constraints and spacecraft size, only limited integrated TVAC testing is possible
  Verification relies heavily on the ITM, coordinated element‑level testing, targeted interface tests, and increased model fidelity and margins where interface testing cannot occur
Inputs from other Disciplines
Reduced Thermal Models (RTMs)
Environments
DSNE
Launch Vehicle
Induced (Plume)
Mission Design
DRMs
Con-Ops
Pointing constraints
Hardware Ops and RQMTs
Power & Dissipation
Thermal Interface Rqmts
Definition of Thermal Interfaces and Induced Environments
Thermal Data Book
ITM for Element’s detailed analysis
Mission thermal performance
SR-1 ITM
Boom
Reactor & PCS
HRS
NPM
Skyfall
PPE

## Slide 6: Nuclear Power Module
New (and old) systems that have never operated in space
High-Assay Low-Enriched Uranium Fission Reactor
  Based on VALKRE design from Idaho National Lab
  < 20% enriched UO2
  Core cooled by sodium heat pipes
    Operates at ~1000 K
Closed Cycle Brayton Power Conversion System
  He-Xe working fluid turbomachinery
  Heat pipe–gas “hot” side heat exchanger
  Gas-liquid “cold side” heat exchanger interface to heat rejection system radiators
  Parasitic Load Radiator resistors regulate turbine speed (~800 K operating temperature)
  ~20% thermodynamic efficiency
Sodium heat pipes
Hot
HX
Reactor Core
Turbine
Compressor
Alternator
Cold
HX
Radiator
PLR

## Slide 7: Heat Rejection System
Radiators are critical to any Nuclear Electric Propulsion architecture
  Thot (reactor) and Tcold (radiators) determine system efficiency
  …but T4 performance of radiators and mass minimization push you to higher Tcold
  Materials limit max temperature
  Must consider reactor fluence (neutrons and gamma) on materials
Design point ~500 K
  Titanium-water heat pipe / polymer matrix composite baseline design
  Considerable IR backload on surrounding hardware
  Pumped fluid trunkline interfaces with PCS HX
  Implies high heater power usage during cold mission phases
Two deployed “wings” flown edge-to-sun
  Independent flow loops
PCS
HX
Pump
Pump
Wing 1
Wing 2

## Slide 8: SR-1 Thermal Challenges
Extremely aggressive launch schedule constrained by Mars launch window
  Severely limits level of thermal testing we can accomplish
Reactor core ~1000 K, must attach to boom structure that can also react launch loads
  Significant mass limitations drove design to a shorten static Boom, led to reactor being much closer to rest of spacecraft
PLR must reject 20 kW at peak, extreme source of IR backload and mounting challenge
Skyfall was designed as free-flyer and spin stabilized
  SR-1 architecture houses Skyfall within a partial enclosure, yet must allow Skyfall adequate ability to radiate to space

## Slide 9: Questions?