## Slide 1: Investigations in the Low Density Shock Tube (LDST)
Brett A. Cruden1, Andrea Fagnani2
1AMA Inc., 2ORAU at NASA Ames
Radiation in High Temperature Gases Workshop
Bari, Italy
Sep. 23, 2026

## Slide 2: Electric Arc Shock Tube (EAST)
The Electric Arc Shock Tube (EAST) is capable of simulating high speed flows relevant to entry problems
Two shock tubes share the same driver:
  High Velocity Shock Tube (HVST) – 10 cm (4”) Aluminum Tube – test section at 7.9 m (L/D=79)
  Low Density Shock Tube (LDST) – 54.3 cm (21.4”) Stainless Steel Tube – test section at 20.7 m (L/D=39)
NEW!

## Slide 3: Low Density Testing
In 2024, we installed the Low Density Shock Tube (LDST) in the EAST Facility
LDST diameter is 5.4x larger than EAST High Velocity Tube
Increased diameter
  Increases test time as PD2 (Roshko/Mirels)
    Enables testing at low density, useful for high mass
    Mars landers
  Increases S/N of optical measurements
  Reduces boundary layer/core flow ratio
    Reduced deceleration
Test Series:
  Test 65B (2024-25): Dragonfly (Titan) high altitude
  Test 68 (2026-27): Air entries, overlap conditions
Chart: Shock Velocity (km/s)
| 17 | 23 | 29 | 46 | 46 | 27 | 17 | 17
10 cm dia., H2/He | 0.25 | 0.1 | 0.1 | 0.25 | 1 | 10 | 10 | 0.25
10 cm dia., Air, N2, CO2, etc | 760 | 760 | 100 | 2 | 0.25 | 0.25 | 0.1 | 0.1 | 1.55 | 760
60 cm dia., Air, CO2 | 0.01 | 0.01 | 5 | 5 | 1.5 | 0.01
Test 65B | 0.03 | 0.03 | 0.09 | 0.1 | 0.3 | 0.09 | 0.03
Test 68 (planned) | 0.1 | 0.2 | 10 | 2.25 | 0.125 | 0.1

## Slide 4: Shock Velocity Profiles
Shock deceleration impacts the enthalpy profile of test gas in the test section
Shown are three tests at 5.2 km/s in HVST (Tests 61,65A) and LDST (65B)
  Noise in test section is due to proximity of sensors: average value reported
  LDST shows less deceleration than Test 65A, but similar to Test 61
Chart: Distance (cm)
| -1734.0930000000001 | -1609.6330000000003 | -1463.6860000000001 | -1358.5935000000002 | -1211.2735000000002 | -1083.3210000000001 | -905.52100000000019 | -781.37850000000026 | -603.57850000000008 | -479.43600000000015 | -301.63600000000019 | -188.60625000000027 | -90.181250000000091 | -52.716499999999996 | -39.064000000000306 | -24.141500000000178 | -18.426500000000033 | -12.711499999999887 | -9.5364999999997053 | -6.3615000000004329 | -3.186500000000251 | -1.1500000000069122E-2 | 3.1635000000001128 | 6.3385000000002947 | 36.5012499999998 | 59.678750000000036
Test 65B, 8 | 5.8688 | 5.2423 | 5.2747 | 5.5501 | 5.5475 | 5.5027 | 5.431 | 5.3844 | 5.4227 | 5.3825 | 5.3246 | 5.2597 | 5.174 | 5.2457 | 5.2392 | 5.2248 | 5.2137 | 5.2131 | 5.1982 | 5.1833 | 5.2143 | 5.2224 | 5.2034 | 5.2013 | 5.2186 | 5.2173
Test 65B, 7 | 7.0379 | 6.0546 | 5.4593 | 5.1709 | 4.9541 | 5.0539 | 5.1798 | 5.1994 | 5.2053 | 5.2101 | 5.2066 | 5.1587 | 5.0775 | 5.1789 | 5.1973 | 5.1734 | 5.1352 | 5.2254 | 5.1761 | 5.1278 | 5.1479 | 5.1629 | 5.1774 | 5.1081 | 5.131 | 5.1148
Test 65A, 4 | 5.5911 | 5.4278 | 5.3283 | 5.3249 | 5.2485 | 5.2205 | 5.233 | 5.1415 | 5.1954 | 5.2538 | 5.2291 | 5.1509 | 5.0777
Test 65A, 5 | 5.5527 | 5.3202 | 5.2733 | 5.226 | 5.2456 | 5.2654 | 5.2036 | 5.1802 | 5.145 | 5.2955 | 5.2261 | 5.1884 | 5.2662 | 5.1453 | 5.1632
Test 61, 17 | 5.2871 | 5.2489 | 5.2421 | 5.2343 | 5.2142 | 5.2515 | 5.2967 | 5.1431 | 5.1598 | 5.2262 | 5.0821 | 5.3388 | 5.3129
Test 61, 16 | 5.1549 | 5.1813 | 5.1288 | 5.1227 | 5.1276 | 5.1921 | 5.1654 | 5.0494 | 5.0115 | 5.1657 | 5.1912 | 5.2061 | 5.2452
Compression Ratio @ 10 cm

## Slide 5: Sample Data – 5.2 km/s
Spectral and spatial radiance data collected on 4 spectrometers (UV not shown)
Spectral features
  CN Red
  CN Violet
No test gas contamination
  Long test times realized
Significant signal ahead of shock
  Believed to be due to reflections from tube wall

## Slide 6: Spectral Comparison – LDST to HVST
Mean spectral radiance within +/-0.5 cm of peak, normalized by Tube Diameter
UV/Visible (330-490 nm)
  Variation within test 15%, tube-to-tube comparisons overlap
Visible (480-890 nm)
  Variation within test series from 1-10%, mean values agree within 5%
Infrared (950-1400 nm)
  5-13% variation within tests, Test 65B averages 12% higher than 65A
Test 61 (2017, not shown) is in general agreement with these data
Chart: UV/Vis
Chart: Vis
Chart: NIR
65A/5 - 5.21 km/s
65A/4 - 5.18 km/s
65B/7 - 5.16 km/s
65B/8 - 5.21 km/s

## Slide 7: HVST/LDST Comparison vs Time
Necessary to convert x-axis to particle time to compare
Quantitative agreement obtained between LDST/HVST
  Shot 65A/4 (greater deceleration) is somewhat an outlier
DPLR/NEQAIR Comparisons:
  Underpredicts peak radiance, except in IR
  Decay rate slower in EAST than prediction
  Cause of offset in shock location not yet determined
  These inconsistencies are known from previous shock tube testing
  Data will be used to improve modeling practices
Chart: 370-490 nm
Chart: 490-890 nm
Chart: 950-1400 nm
Notes: Note density

## Slide 8: Scattered Signal
All signals are normalized to maximum
Raw signal shown as dotted lines
Pre-shock signal can be due to dark charge or scattered light: Solid lines are corrected signal
Shot 9 had early trigger : shows 10-15% of peak signal after subtraction
Indicates pre-shock signal may be real – suggests scattering in the tube
Shot 8 – 5.21 km/s
Shot 9 – 4.53 km/s
Chart: Distance (cm)
Chart: Distance (cm)

## Slide 9: Specular reflectance
Radiance Measured is a convolution of the actual radiance with a spatial resolution function (SRF):
The optics subtend a biconic volume, which produces the optical portion of the SRF (Cruden, 2014):

## Slide 10: Specular reflectance
Each reflection extends the volume with reflectance
Equivalent to propagating the cone through successive tube diameters (ignoring wall curvature)
2
3
3
2
4
5

## Slide 11: Diffuse Reflectance
For diffusely reflecting wall:
0 reflections: bi-conic SRF0 as given previously
SRF0

## Slide 12: Diffuse Reflectance
For diffusely reflecting wall:
0 reflections: bi-conic SRF0 as given previously
1 reflection: Conical wall transfer function:
Diffuse transfer through medium to wall:
Convolve:
gwall
gdiff

## Slide 13: Diffuse Reflectance
gwall
gdw
=
gdiff
For diffusely reflecting wall:
0 reflections: bi-conic SRF0 as given previously
1 reflection: Conical wall transfer function, convolved with diffuse collection through the medium
2 reflections: Conical wall transfer function:
Diffuse wall transfer function:
Collection through the medium:
Convolve:

## Slide 14: Diffuse Reflectance
For diffusely reflecting wall:
0 reflections: bi-conic SRF0 as given previously
1 reflection:
2 reflection:
N reflections:
Conical wall transfer function
N diffuse wall transfer functions
Collection through the medium
gwall
gdw
gdiff

## Slide 15: Compare SRFs on Step (Heaviside) Function
Examine impact of SRFs on shock as a step function, compare to Shot 9
Specular reflections do not capture the shape of the data
Diffuse reflections with reflectivity near 0.5 in reasonable agreement with shape
Diffuse reflections span multiple tube diameters (100s of cm)
Specular
Diffuse

## Slide 16: Reflectance Correction
Assume radiance rises and falls exponentially and convolve with camera and diffuse SRF
Multi-parameter fit to data returns reflectance and functional parameters
Correcting data by subtracting the pre-shock reduces scattered contribution from 11% to 4%
Error in the peak signal ~4%, error at edge of domain ~10%
Subtract
Pre-shock

## Slide 17: Comparsion to HVST (10 cm tube)
Reflection contribution much smaller in HVST
More attenuation at smaller radius
Lower Reflectance from HVST walls
UV/Vis
Vis/NIR

## Slide 18: Non-reflective Coating
Adding non-reflective strip to opposite wall reduces pre-shock signal substantially
A non-outgassing black coating was applied to inserts on the opposite wall
Will be deployed in next test series
Chart: Position (cm)
w/coating (6 km/s)
w/o coating (5.7 km/s)

## Slide 19: Conclusion
Low Density Shock Tube (LDST) in EAST is operational
Initial series performed for Dragonfly (Titan) entry conditions
LDST shows much longer test times, lower deceleration
Initial data shows quantitative agreement to data collected in High Velocity Shock Tube (HVST)
  Spatial axis must be converted to Lagrangian (Time of Flight) basis
Issues identified and being addressed
  Pre-shock signal caused by diffuse reflections mitigated by non-reflective coating
  Non-planarity with Helium/Argon mixtures addressed through driver loading panel
Presently starting repeat of air testing studied in HVST
Low density Mars/Venus testing next year

## Slide 20: Contributors
EAST Facility Staff
Ramon Martinez
Rick Ryzinga
Alex Contreras
Ryan Chung
LDST Design
Daniel Schickele
Trent Hughes
Daniel Philippidis
Frank Lesperance
Research Staff
David Bogdanoff
Andrea Fagnani

## Slide 21: Backup

## Slide 22: First Test Series in LDST (Test 65B, Dragonfly/Titan)
Shocks from 3-8 km/s in Titan simulant (2.2% CH4 in N2) are performed for Dragonfly Mission
The “Shock Tube Informed Bias” Approach is used to compare to radiative heating on vehicle backshell1
  These will be compared to radiometers installed on the vehicle backshell (Dragonfly Entry Aerothermal Measurement – DrEAM)
Test 65A was conducted in HVST in 2021 at (mostly) 0.2 Torr and Above2
Test 65B includes 0.09 and 0.03 Torr conditions for early trajectory points3
  Includes overlap to Test 65A
1Johnston, C.O. “Evaluating Shock-Tube Informed Biases for Shock-Layer Radiative Heating Simulations," JTHT 2021.
2Tibère-Inglesse, A. C., Johnston, C. O., Brandis, A. M., and Cruden, B. A. "Backshell radiation measurements in the EAST facility for Titan entry," AIAA AVIATION 2023 Forum, 2023.
3Fagnani, A., Brandis, A. M., and Cruden, B. A. "Characterization of Titan Entry Radiative Heating in the Low Density Electric Arc Shock Tube," AIAA SCITECH 2025.
4Fagnani, A., et al. "Assessment of CN non-Boltzmann kinetics against Low Density Shock Tube data," AIAA SCITECH 2026.
veff
deff
Chart: Lab Pressure (Torr)
| 0.03 | 0.09 | 0.21 | 0.3 | 0.4 | 0.65 | 0.91 | 1.1499999999999999
Dragonfly Candidate | 7.27 | 6.99 | 6.42 | 6.06 | 5.62 | 4.76 | 4 | 3.39
Huygens | 6.0923 | 6.0989 | 6.1044 | 6.1071 | 6.1019 | 6.0713 | 5.9767 | 5.733 | 5.1861 | 4.2257 | 3.0448 | 2.0254
Test 65A (HVST) | 6.9658 | 5.4751 | 5.8363 | 5.1762 | 5.212 | 4.3853 | 4.2251 | 3.9981 | 4.1089 | 3.915 | 4.6348 | 5.0884 | 5.3316 | 5.1985 | 5.8721 | 5.3858 | 5.655 | 4.3906 | 3.91 | 3.5959 | 3.807 | 3.6648 | 4.4394 | 5.3813 | 5.1816 | 4.9084 | 3.7486 | 3.4257 | 3.6074 | 3.8687 | 4.0335 | 4.3301 | 4.2012 | 5.1258 | 4.865 | 5.0359 | 4.6571 | 3.7228 | 3.94 | 3.8843 | 4.3076 | 3.5127 | 3.504 | 4.6495 | 4.8244 | 4.1209 | 5.3456 | 3.5546 | 3.472 | 3.0942 | 3.25 | 3.1894 | 3.1303 | 5.4738 | 4.0801 | 5.2942 | 4.7354 | 4.3664
Test 65B (LDST) | #N/A | 2.968 | 4.1782 | 5.7224 | 6.2253 | #N/A | 5.1582 | 5.205 | 4.5303 | 3.8 | 4.094 | 4.0494 | 4.6864 | 4.6383 | 4.8885 | 5.7167 | 5.4916 | 5.6732 | 3.8692 | 4.5517 | 4.4533 | 5.2424 | 4.8652 | 5.11 | 6.0932 | 5.8995 | 5.8187 | 6.6982 | 6.7504 | 6.5354 | 6.6559 | 6.4991 | 7.068 | 5.9516 | 6.462 | 5.6908 | 5.7196 | 6.2898 | 5.4479 | 4.0143 | 3.9525 | 4.0255 | 3.9417 | 4.164 | 6.4521 | 6.3145 | 2.0618 | 6.9197 | 6.2664

## Slide 23: Testing at low density
Around 2011, HEDL project expressed interest in low density testing for high mass mars landers, e.g. HIAD, ADEPT
Difficulty achieving sufficient test time, signal in HVST at these conditions
The LDST should achieve longer test times based on Mirels (Roshko) Theory (1963)
  t ~ PD2
    At 6x diameter, possible 36x increase in test time
    Actual gain is less than this due to length scaling
A series of tests were performed in the 24” Low Density Shock Tube (LDST) from 2012-15
  Quality of shots was generally poor
  Attributed to quality of fabrication of tube
  It was decided to construct a replacement for LDST
Fabrication of new LDST started ~2020
New LDST became operational in late 2024
4” HVST
Old 24” LDST
Radiation Observed
Integrated over tube diameter
And through the boundary layer

## Slide 24: Spatial Comparison – LDST to HVST
Chart: 370-490 nm
Chart: 490-890 nm
Chart: 950-1400 nm
Radiance vs distance from shock front
Comparing 2 Shots from each tube
Nominally 5.2 km/s and 0.1 Torr
Normalized by Tube Diameter
  65A – HVST (10.16 cm)
  65B – LDST (54.31 cm)
Intensity at peak generally agrees between tubes

## Slide 25: Spatial Comparison – LDST to HVST
Chart: 370-490 nm
Chart: 490-890 nm
Chart: 950-1400 nm
Comparing radiance vs distance from shock
Results diverge ~4 cm from shock
DPLR/NEQAIR
  Peak is generally delayed relative to camera alignment
  CN Violet peak is lower, trends between LDST and HVST
  CN Red peak is later, trends with LDST data

## Slide 26: Spatial Comparison –Time of Flight
Test Gas
Driver Gas
x
Clarke, et al. (2023), recognized spatial transform required
This is due to the deceleration of gas from the shock front to the contact front
Time spent in the flow is the integral of velocity:
Data can be compared on a Lagrangian, or time-of-flight, basis:
Shock frame of reference
v=0
v=0
v∞ = vs
v<<vs
L
ρ∞, T∞
Chart: 
Notes: Use density based on CFD simulation

## Slide 27: Time of Flight HVST vs LDST
0g
HVST
LDST
Chart: x (cm)
LDST has 5.4x diameter
Maximum slug length is 28x larger than in HVST
Actual slug length (at test section) is 10x larger
v > 0 at end of slug
  Contact front continues moving backward with particle
For measurement at a particular time/location
  TOF calculation should use maximum slug length
  Data not obtained beyond the actual slug length
The time of flight on HVST is longer than on LDST
Max Slug
Actual Slug
v>0
HVST
LDST

## Slide 28: Combined Diffuse + Reflective
Consider n total reflections, with m specular
Relationships get complicated, embedded sums:
A recursive algorithm is written to compute the combinatorics

## Slide 29: Combined Specular+Diffuse vs Data
Fix diffusive reflectance at 0.5, vary specular reflectance
Fit is not unique, but R>0.1 seems necessary
Specular reflectance leads to potentially significant overestimates of radiance

## Slide 30: Pre-shock signal – Scattered Light
Pre-shock signal persists for several cm in front of shock arrival
A scattering function is analytically derived which acts as a convolution on the unscattered signal
Influence of scattered radiation spans multiple tube diameters (100’s cm), depends on signal measured outside of spectrometer image
4.53 km/s, 0.09 Torr
Chart: Distance (cm)

## Slide 31: Scattered Light Correction
Scattered signal is about 10% of the peak signal, but ~30% of signal at camera edge
Scattering model shows scattered signal before shock is smaller than post-shock signal
Subtracting the pre-shock signal leaves <6% error in post-shock signal

## Slide 32: The Arc Driver
0 kV
0 kJ
Up to 40 kV
1.3 MJ
In EAST, shocks are propelled by Arc Driver
The “30 inch” driver is the preferred driver for LDST but has not been used much in last 20 yrs.
Arc Driver gives high T4 – O(10,000K), increases shock speed by >5x over cold driver
Energy Pressure far exceeds the fill pressure – O(1 MPa)
Diaphragm rupture pressure typ. 1/2PE

## Slide 33: Driver Optimization
0 kV
0 kJ
4 kV
12 kJ
Poorly chosen driver conditions may not fully discharge the capacitor bank
Reflected shock return causes secondary discharge which damages the driver
Necessary to reduce pressure, add Argon and/or increase Voltage to reduce “Arc-out”
Increasing voltage raises shock speed – Add Argon to tune the velocity
15 kV
170 kJ
Chart: Voltage (kV)
| 9.4 | 13.5
Test 42, 100 psi He | 4.25 | 4
Test 42, 100 psi, 50% Ar | 2 | 3 | 2.5 | 2 | 1.75
Test 42, 220-300 psi He | 9 | 5.5 | 6.25 | 5.5
Test 35, 325 psi He | 6.5 | 5.5 | 6.25 | 9.5 | 4.5
Test 35, 325 psi, 33% Ar | 1.15
100-120 psi He | 1.7 | 1 | 1.1 | 1.25 | 1.95 | 1.95 | 2.3 | 3.9
Test 63, 200 psi He | 2.2 | 3.2
Test 63, 400-490 psi He | 9 | 15.6
Test 63 rebuilt, 200 psi He | 8.7
Test 65B, 200 psi, 40% Ar | 1.7
Test 65B, 200 psi, 5% Ar | 4.2
Chart: 
| 24 | 24 | 24.5 | 25 | 25.2 | 25 | 25 | 24.5 | 25.5 | 25 | 26 | 25 | 24.5 | 24.75 | 22 | 25 | 24 | 25 | 25 | 25 | 25 | 25 | 24.6 | 25 | 24.6 | 24.1 | 24.4
This Test | 1.2 | 1.5 | 1.2 | 1.1 | 0.9 | 1.2 | 1.2 | 0.9 | 1 | 1.5 | 1.6 | 2 | 2.1 | 1.36 | 1.28 | 1.25 | 1.05 | 0.81 | 0.81 | 0.93 | 1.44 | 1.44 | 1.64 | 1.723 | 1.058 | 2.508 | 2.219
Chart: 
| 0 | 0 | 0 | 0.4499999999999999 | 0.3 | 0.35 | 0.65 | 0.6 | 0.6 | 0.75 | 0.75 | 0.75 | 0.75 | 0.75 | 0.8
0.03 Torr | 3.8692 | 4.5517 | 4.4533 | 5.2424 | 4.8652 | 5.11 | 6.0932 | 5.8995 | 5.8187 | 6.6982 | 6.7504 | 6.5354 | 6.6559 | 6.4991 | 7.068
0.09 Torr | 5.7224 | 6.2253 | #N/A | 5.1582 | 5.205 | 4.5303 | 4.094 | 4.0494 | 4.6864 | 4.6383 | 4.8885 | 5.7167 | 5.4916 | 5.6732

## Slide 34: Driver Mixing/Planarity
Chart: 
Observed a loss of planarity when Helium % exceeds ~60% (v > 6 km/s)
For 0.7 MPa initial pressure, the Ar-He diffusion length is ~5 cm in 5 min
Increasing settling time to ~40 minutes improved planarity
Future plan to load gases simultaneously to improve mixing
Chart: 
| 0.75 | 0.75 | 0.75 | 0.8 | 0.8 | 0.8 | 0.7 | 0.7 | 0.7 | 0.1 | 0.15 | 0.15 | 0.15 | 0.4 | 0.4
4-point | 2.0572 | 4.4028 | 0.68458 | 12.474 | 9.168 | 10.321 | 0.21174 | 0.30455 | 4.9304 | 0.27132 | 0.20693 | 0.14142 | 0.87658 | 0.36119 | 0.23578
Horizontal (2 pt) | 0.14677 | 0.045738 | 0.16229 | 0.16494 | #N/A | 0.027212 | 0.0061311 | 0.87748 | 0.3772 | 0.26307 | 0.049044 | 0.21587 | 0.90369 | 0.067323 | 0.039272 | 0.042523 | 0.16982 | 0.50943 | 0.21675 | 0.47826 | 0.09972 | 0.14194 | 3.5573 | 0.21936 | 0.40156 | 2.0856 | 0.39254 | 1.3847 | #N/A | #N/A | 0.14998 | 7.8089 | 0.042446 | 0.029721 | 0.24153 | 5.0482 | 0.15103 | 0.012379 | 0.096851 | 0.98773 | 0.36731 | 0.13676 | 0.19356 | 0.050671 | 0.13272 | 0.068063
With Settling | 0.23578 | 0.42736 | 0.40986 | 0.011518 | 0.48873
Gas Load

## Slide 35: Mixed Gas Loading
A gas loading panel for the driver was designed
Gas loading panel delivers Ar and He in controlled ratio simultaneously, eliminating Ar/He stratification
Old Panel
New Panel